## Slide 1
Data-Driven SoC Floorplanning
ICCAD 2026 FloorSet Problem C | Physical Design Automation Final Project
Architecture v5 solver for contest-style SoC floorplanning
Anchor-GNN guidance as geometric prior
Deterministic decoder, repair, diagnostics, and v10 ranking
Promotion by full-validation no-runtime evidence with runtime gates
1

## Slide 2
Problem and Scoring Pressure
Input: blocks, target areas, b2b/p2b connectivity, pins, and constraints
Output: one (x, y, width, height) rectangle for every block
Hard constraints: no overlap, area tolerance, fixed-shape, preplaced geometry
Soft constraints: boundary, grouping connectivity, and MIB shape consistency
v10 case weights grow approximately as exp(n/12), so large and dense cases dominate risk
2

## Slide 3
Core Design Idea
Learned priors should guide placement, not replace the floorplanner
Anchor-GNN predicts geometry, priority, aspect ratio, and pairwise orientation
Production Solver Path remains deterministic and legality-aware
Encoder experiments do not change decoder, repair, or ranking contracts
Architecture decisions are promoted by total_score_no_runtime, then checked by runtime gates
ML prior + physical-design legality + evaluator evidence
3

## Slide 4
Architecture Evolution: What Changed and Why
Stage | Main attempt | Reason for change
arch-v1/v2 | Initial learned path, wrappers, hetero graph, relative-order decoder | GNN guidance still needed deterministic repair and stable solver contracts
arch-v3 | Pairwise heads, training/checkpoint experiments | Validation loss was not enough; evaluator evidence became promotion signal
arch-v4 | No-runtime score and runtime diagnostics | Local runtime-aware score could distort architecture tuning
v5 | Graph Transformer and selectable encoder contract | Richer constraint context without changing downstream solver path
v10 branch | Proxy-first ranking, conditional budget, narrow grouping | Soft-first and broad knobs regressed quality or runtime
4

## Slide 5
Architecture v5 Production Flow
Evaluator tensors
parse_instance()
Instance
_try_anchor_guidance()
AnchorGuidance
candidate specs + budget
relative_order / opt-in beam
repair_placement()
placement_metrics()
v10_proxy_rank()
best Placement -> evaluator output
Stable contracts: Instance and Placement move through every stage.
5

## Slide 6
Selectable Anchor-GNN Encoder
MPNN: block features plus weighted block-to-block edges
Graph Transformer: block graph plus pin, cluster, MIB, and boundary context edges
Local HGT: typed block, pin, cluster, MIB, and boundary nodes with relation-specific attention
All encoders emit the same heads: anchor, priority, log_aspect, pair_logits
Runtime adapter converts shared heads into AnchorGuidance(rect_priors, priority, log_aspect, pairwise_axis)
6

## Slide 7
Constraint-Aware Decoding and Repair
relative_order.construct_relative_order_placement() is the main constructive decoder
Decoder uses anchor priors, connectivity, constraint statistics, and profile-specific ordering
pairwise_axis biases ambiguous horizontal/vertical pair relations
Narrow grouping pair bias applies only to ambiguous same-cluster pairs under pressure
Repair fixes hard geometry first, then boundary, grouping, and MIB soft constraints
7

## Slide 8
V10 Ranking and Evidence-Gated Budget
hard legality rank
v10 no-runtime proxy cost
soft-constraint key
HPWL / bbox quality key
Risk features: score_share, constraint_density, net_density
Budget tiers: NONE, LIGHT, MEDIUM, HEAVY
Extra candidates, soft repair, and quality portfolio pass through the budget layer
Conditional runtime budget stops only extra work after rejected attempts or elapsed limits
8

## Slide 9
Training and Checkpoint Promotion
Dataset samples and fp_sol are parsed into Instance objects
Pseudo-target logic separates clean, dirty, and repaired targets
Shared heads are trained with anchor, aspect, priority, and pairwise relation losses
Dirty samples are weighted so soft-violating golden answers do not become constraint oracles
Promotion priority: total_score_no_runtime -> tail no-runtime -> soft violations -> avg runtime
9

## Slide 10
Current Evaluation Evidence
Run | No-runtime | Total | Feasible | Avg / P90 / Max | Decision
Merge-base baseline | 2.2184 | 2.7762 | 100/100 | 1.25 / 2.27 / 7.01s | baseline
Phase 1 v10 proxy | 2.1634 | 2.7471 | 100/100 | 1.24 / 2.12 / 7.42s | keep default
Phase 1 + narrow grouping | 2.1538 | 2.6993 | 100/100 | 1.23 / 2.24 / 6.58s | promote default
Phase 1 + soft repair | 2.1446 | 2.8314 | 100/100 | 1.40 / 2.46 / 9.64s | opt-in only
Soft repair + conditional budget | 2.1670 | 2.7207 | 100/100 | 1.22 / 2.56 / 5.70s | runtime useful
10

## Slide 11
Takeaways and Next Steps
Learned geometry is a prior; deterministic solver logic preserves legality
Instance and Placement are stable contracts across decoder, repair, diagnostics, and ranking
Selectable encoders are compared through the same AnchorGuidance interface
v10 changes are promoted only when full-validation evidence and runtime gates agree
Next: tighter soft-repair gates and quality-first HGT retraining with evaluator-backed promotion
11

## Slide 12
Backup: Prior Attempts and Outcomes
Attempt | Observed result | Decision
Large-case matrix | No-runtime tied default at 1.9560; tail deltas were zero | opt-in only
No-checkpoint mode | Feasible but much worse no-runtime: 4.6289 vs 2.0326 | repair diagnostic
Quality portfolio | HPWL headroom but runtime-aware and later no-runtime regressions | opt-in only
V10 soft repair | Small no-runtime gain but runtime tail risk | opt-in with budget
Hard runtime clamp | Reduced tail runtime but over-clamped quality | removed
Broad grouping bias | Regressed no-runtime and total | removed
12

## Slide 13
Backup: Evidence Policy
Do not promote from single-case wins or validation IDs
Do not promote checkpoints from supervised validation loss alone
Use total_score_no_runtime for architecture comparison
Use raw runtime, P90, max runtime, and runtime-aware total as submission gates
Keep mixed-evidence controls as explicit ablations
13